Soft-Error-Analysis

---
Typical Synthesis Flow
Overview
- Introduction: Soft-Errors & Soft-Error Analysis
- Detect Soft-Errors
- Verify protection Logic (main part)
  - input format, algorithms, output format, ..
- First results
- Conclusion / future work

---
Soft Errors
- Boolean circuits: inputs, AND gates, latches, outputs
- Components (latches, AND gates) can have soft-errors
  - flip truth value
  - Single fault assumption (only one component flips)

---
Soft-Error-Analysis
- Circuits to detect soft-errors aka protection Circuit:
  - Alarm output: true, when flip has an effect on the value of the outputs
- Main goal of my work: create Tool that tests the soft-error-detection for completeness (semi-formally ;-):
  - Report definitely vulnerable and potentially protected circuits
Simplified view:
alarm circ
alarm output
Sequential
circuit
Inputs
Outputs
openSEA

---
How to detect Soft-Errors?
L1
L2
Outputs
...
...
Inputs
Ln
...

---
How to detect Soft-Errors:
→ add redundancy! New Tool: AddParityTool
L1
⊕
Inputs
L2
Outputs
...
...
⊕
Alarm Output
Ln
⊕
Le1
⊕
⊕
...

---
How to detect Soft-Errors:
- AddparityTool:
- Input:
  - Circuit to protect (in AIGER format)
  - Percentage of latches to protect
  - New latch per how many existing latches (k)
    - Relevant for critical circuit depth
- Output:
  - Protected circuit
  - With new output: alarm
  - Contains k extra latch(es)
Alarm Output

---
Is the protection-circuit correct ... ?
- ... or is there some scenario where a latch can be flipped without recognizing that?
- which latches are definitely vulnerable?
- which are potentially protected?
?
out
in
?
?

---
Is the protection-circuit correct ... ?
- ... or is there some scenario where a latch can be flipped without recognizing that?
- which latches are definitely vulnerable?
- which are potentially protected?
- The openSEA (tool) can help you with these questions!
  - open Soft-Error-Analysis – a tool to verify protection circuits (working title)

---
openSEA
- Input: arbitrary circuit with protection logic (alarm output)
- Output: List of definitely vulnerable latches
- highly modular, extensible and configurable
- several algorithms, modes, options, optimizations, ...
Vulnerabilities:
L1, L334, …,
L9985
AIGER circuit
BackEnd:
SimulationBased
[TestCase(s)]
SymbTime
[Error-Traces]:
Latch 1:
- flip L1 at i=5
- error at i=9
- input vectors
i0: 0101
i1: 1010
...
Options
SymbTimeLocation
Lingeling
miniSAT
PicoSAT
openSEA

---
Input and Output Format
- Input Format:
  - circuit with protection logic
  - TestCase(s) consisting of a vector of input values
time	Input 0	Input 1
ts 0	1	1
ts 1	0	1
ts 2	1	0

---
Input and Output Format
- Output Format:
  - List of definitely vulnerable Latches
  - Optional: ErrorTraces for each vulnerable Latch (to stdout or to file)
    - When happens the flip, when has it an effect on the output, what were the necessary inputs?
L3
L42
L1337
L3:
Flip at ts 10
Wrong output at ts 13
time	Input 0	Input 1
ts 0	1	1
ts 1	0	1
ts 2	1	0

---
BackEnd: SimulationBasedAnalysis
1. Execute correct simulation with the provided TestCase (vector of input-vectors)
  store the resulting output vectors
2. Compare with all possible faulty simulations
  for each latch:
  for each time-step: flip truth value of latch ( = timestep i )
    vulnerable, if output value is different in this or in a future-time-step ( = timestep j )
Implementational Details:
- Implemented AIGER circuit simulator for that

---
BackEnd: SymbTimeAnalysis (1)
Idea: make point in time where a latch value is flipped symbolic, call SAT-Solver
- Do for each latch:
- Convert circuit to a CNF transition relation (Tseitin transformation)
- Unroll transition relation for each timestep in the TestCase
  - replace input variables with concrete input values from TestCase
  - append modified copy each iteration, previous state to next state
  - add clause(s) saying that the output has changed
  - call SAT solver
timestep n:
timestep 0:
timestep 1:
L(0)
L(1)
0
1
0
1
0
1
replaced
Latch-output
replaced
Latch-output
...
f0
f1
fn

---
BackEnd: SymbTimeAnalysis (2)
assignment: ¬f0, f1, ¬f2, .. , ¬fn
- If SATISFIABLE:
  - current latch is vulnerable
  - SAT assignment: read point in time where a flip creates an error (f variable)
timestep 0:
timestep 1:
timestep n:
L(0)
L(1)
0
1
0
1
replaced
Latch-output
replaced
Latch-output
...
Implementational Details:
- Incremental SAT solving
- mode: don't copy whole transition-relation, build CNF on-the-fly
f0
f1

---
BackEnd: SymbTimeLocationAnalysis (1)
Idea: make point in time AND the latch to flip symbolic
...
timestep n:
timestep 0:
L1
(0)
L1
(n)
Latch 1:
0
1
0
1
...
0
1
replaced
Latch-output
0
1
replaced
Latch-output
c1
f0
fn
c1
Lm
(n)
Lm
(0)
0
1
0
1
Latch m:
0
1
0
1
replaced
Latch-output
replaced
Latch-output
...
fn
cm
cm
f0
...
...
...
...

---
BackEnd: SymbTimeLocationAnalysis (2)
- If SATISFIABLE:
  - Found vulnerability
  - SAT assignment:
    - c3: Latch 3 is flipped
    - f1: it is flipped in timestep 1
assignment: ¬f0, f1, ¬f2, .. , ¬fn, ¬c1, ¬c2, c3, .., ¬cm

---
BackEnd: SymbTimeLocationAnalysis (3)
- Unroll transition relation for each timestep in the TestCase:
  - append modified copy each iteration, previous state to next state
  - replace input variables with concrete input values from TestCase
  - clause(s) saying that output has changed

---
Extension: TestCase with free Input-Values
- allows TestCases to have undefined input-variables
- For SymbTimeAnalysis and SymbTimeLocationAnalysis
- Not (easily and efficiently) possible for SimulationBasedAnalysis
- SAT-solver chooses the values for inputs to force an error
- Example TestCase with free inputs & Example Error-Trace
time	Input 0	Input 1
ts 0	1	1
ts 1	1	?
ts 2	?	0
L3:
flip at ts 10
Wrong output at ts 13
time	Input 0	Input 1
ts 0	1	1
ts 1	1	1
ts 2	0	0
…
…

---
Extension: TestCase with free Input-Values
- Get the best of both worlds:
  - Discrete input values when possible (faster!)
  - Variable input values when necessary (flexible)
- This makes OpenSEA a full model-checker!
  - With detailed feedback for the hardware designer where the bug is
L3:
flip at ts 10
Wrong output at ts 13
time	Input 0	Input 1
ts 0	?	?
ts 1	?	?
ts 2	?	?
time	Input 0	Input 1
ts 0	1	0
ts 1	0	1
ts 2	0	1
…
…

---
What else have I done?
Convert circuit with protection logic to a model-checking problem (standalone tool):

---
What else have I done?
Start running some benchmarks on the developed
algorithms with several modes, optimizations, etc., on problem-
instances
Execution time of the first 4 modes
time [s]

---
What else have I done?
A lot of coding

---
What else have I done?
drinking Coffee ;-)

---
Conclusion
- AddParityTool: adds simple parity computation to protect a circuit
- Create configurable SEA Tool: openSEA
- Implement Soft-Error-Analysis Algorithms:
  - Simulation-Based Analysis
  - SAT-Based: Symbolic Time
  - SAT-Based: Symbolic Time + symbolic Location
- Optimizations, Free Inputs extension
- Implement pure Model-Checking Approach as well
- First Benchmarks

---
Future Work
- more benchmarking
- quantitative analysis: how likely is each vulnerability
- Check other components for vulnerabilities:
  - Besides of latches, AND gates could be flipped as well
- Detect false alarms
- Model an environment and add exceptions:
  - output might not be relevant at each timestep
- … and lots of other things you can think of

---
  Questions?
  Thank you for your attention!