Soft-Error Analysis

---
Typical Synthesis Flow
Overview
- Introduction:
  - Soft-Errors
  - Protection Logic
  - Classification of components
- Techniques:
  - simulation vs. formal vs. semi-formal
- Algorithms (application of the techniques for classification)
- Benchmark Results

---
Soft Errors / Faults
- Sequential Boolean Circuits: inputs, AND gates, latches, outputs
- Components (latches, AND gates) can suffer from faults
  - flip truth value
- Single fault assumption

---
Protection Logic
- Special part of a circuit for reliability
- Detect faults or correct faults
- Examples: Triple Modular Redundancy (TMR), parity-checks, ...

---
How to correct errors: TMR Example
- Example: triple modular redundancy
- Con: > 200% overhead in power consumption and area!
f(in)
f(in)
f(in)
out
in
majority gate
a
b
c

---
How to detect errors?
L1
L2
Outputs
...
...
Inputs
Ln
...

---
How to detect errors:
→ add redundancy.
L1
⊕
Inputs
L2
Outputs
...
...
⊕
Alarm Output
Ln
⊕
Le1
⊕
⊕
...

---
Errors in protection logic
- vulnerable latches
  - Faults that corrupt primary outputs
    → soft error escaped
- false positives
  - Unnecessarily reported faults
no alarm raised
flip
output
different
somewhere:
alarm raised
outputs OK
flip

---
Techniques for Component Classification
- Simulation
  - Not Complete
  - Fast, good scalability
- Formal methods
  - Complete
  - Slow, bad scalability
- Semi-Formal methods
  - Flexible
Completeness
Scalability
All Inputs Fixed	Some Inputs Open	All Inputs Open
Simulation		Formal (MC)
Semi-Formal

---
Detecting vulnerable latches
- Formal method: (Bounded) Model Checking
- Simulation
- Semi-formal methods
no alarm raised
flip
output
different

---
Formal: Model Checking Approach
Circuit
Output1
Input
Alarm
E (“soft error
escaped”)
clock
State
Copy
Output2
Input
Alarm
clock
clock
State

---
Simulation (1/2)
- Test case provides input values for the circuit:
  (1) Execute correct simulation
  (2) Execute faulty simulations
  - Induce faults
  - Compare output values with correct simulation
01101000110
10101100111
…
  for all latches l in L:
    for all time steps i=1 to len(t):
      // check if soft error injected at
      // latch l in step i of test case t
      // escapes (now or in future steps)

---
Simulation (2/2)
- Not complete! (only concrete test cases)
- But: might already find some vulnerable latches / false positives
- Fast for a single test case
- Not suited for verification

---
Semi-Formal approach
- Sequential Equivalence Checking
- SAT-based: symbolically encode the circuit as a formula
- test case-based: Input values from test cases, can be concrete or open
- point in time AND component to flip symbolic
011??01000110
101??01100111
…
  for all latches l in L:
    for all time steps i=1 to len(t):
      Flip latch
//check ...

---
Convert circuit to CNF formula (for SAT-solver)
Circuit can be converted to a transition relation formula T(x,i,o,x’)
talks about inputs, outputs, current- and next state
Execution of circuit: T(x0,i0,o0,x1) ∧ T(x1,i1,o1,x2) ∧ … ∧ T(xn,in,on,xn+1)
0:
1:
n:
01 …….... 0
1? ……..... ?
…
?? ……….. ?
time step n:
time step 0:
time step 1:
T(x0,i0,o0,x1)
T(x1,i1,o1,x2)
T(xn,in,on,xn+1)
...
 I 0
...
...
Initial state x0
i1
 I 1
i1
 I n
O0
i1
o1
i1
on

---
Semi-Formal Algorithm
- Sequential Equivalence Checking: compare fault-free and faulty circuit
- SAT-based: symbolically encode the execution of both circuits as a formula:
  - fault-free: T(x0,i0,o0,x1) ∧ T(x1,i1,o1,x2) ∧ … ∧ T(xn,in,on,xn+1)
  - faulty: T(f0, c, x’0,i0,o’0,x’1) ∧ T(f1, c, x’1,i1,o’1,x’2) ∧ … ∧ T(fn, c, x’n,in,o’n,x’n+1)
  - c defines which latch should be flipped, f defines the point in time when it should be flipped
- test case-based: Input values i from test cases, can be concrete or open
011??01000110
101??01100111
…

---
SAT-query to find vulnerable components
- If SATISFIABLE:
    - c3: Latch 3 is flipped
    - f1: it is flipped in time step 1
    - Output wrong in step i (at query time)
  for all time steps i=1 to len(t):
      “Dear SAT solver, can you produce a wrong output at step i without
       alarm raised by flipping any latch in some earlier step?”
assignment: ¬f0, f1, ¬f2, .. , ¬fn, ¬c1, ¬c2, c3, .., ¬cm
…

---
Detecting definitely protected latches
- must hold in any state!
- Definitely protected → not vulnerable
- Not definitely protected → ??? (maybe protected, maybe vulnerable..)

---
Detecting definitely protected latches
- Check property using a SAT-solver
- k-step protection of a latch:
  A fault in any state (an over-approximation of all states) ...
  a) … either gets masked out within at most k time steps
          ( and does not affect any outputs)
  b) … or an alarm is raised within at most k time steps
         ( and does not affect any outputs before)

---
False Positives
- Problem: impossible to compare outputs forever
  - undecidable
- Solution: search for situations where the state is repaired within finite time
  - Incomplete: might not find all false positives
somewhere:
alarm raised
outputs OK (forever?!)
flip
somewhere:
alarm raised
outputs OK
flip
state normal again

---
Detecting false-positives
- Formal method: (Bounded) Model Checking
- Simulation
- Semi-formal methods
somewhere:
alarm raised
outputs OK
flip
state normal again

---
SAT query to find false positives
- Find situations where
  - bit flip raises an alarm, does not corrupt outputs, and state recovers from bitflip
  for all time steps i=1 to len(test-case):
      “Dear SAT solver, can you find a false positive by flipping
  any latch in any previous time step?”
- If SATISFIABLE: false positive found
    - c3: Latch 3 has to be flipped
    - f1: it has to be flipped in time step 1
    - state ok again in step i (at query time)
assignment: ¬f0, f1, ¬f2, .. , ¬fn, ¬c1, ¬c2, c3, .., ¬cm

---
Summary
- Properties to check
  - Search for vulnerable components
  - Prove that component is definitely protected
  - Find situations for false positives
- Techniques for checking:
Completeness
Scalability
All Inputs Fixed	Some Inputs Open	All Inputs Open
Simulation		Formal (MC)
Semi-Formal

---
Results – simulation vs semi-formal (1/2)
- Simulation vs semi-formal (point in time and component to flip are symbolic variables)
- 3 concrete test cases, each 15 time steps long
- Search for vulnerable latches
011010001110
101011010111
…
benchmarks (add)
time [s]

---
Results – simulation vs semi-formal (2/2)
- 3 test cases, each 15 time steps long, containing some open input values
- Search for vulnerable latches
- >5 open inputs: semi-formal faster, < 5: simulation faster, ~5: about the same
011??01000110
10101??110111
…
a) simulation with (some) free inputs
benchmarks
time [s]
b) semi-formal approach with (some) free inputs
benchmarks
time [s]

---
Conclusion
- Open inputs: Semi-formal algorithms scale significantly better than simulation
- Concrete Inputs: Simulation is fastest
- Reducing input space: better than MC
011??01000110
10101??110111
…

---
Thank you for your attention!
Questions?

---
formal vs semi-formal method
- All inputs open (MC and semi-formal) vs. all inputs concrete (semi-formal)
- Search for vulnerable latches
- Semi-formal method and BMC about the same performance with all inputs open
- Semi-formal can be faster by setting (some) inputs to concrete values
benchmarks
time [s]
???????????????
???????????????
…
011010001110
101011010111
…

---
OpenSEA
- Input: arbitrary circuit with protection logic (alarm output)
- Output: List of definitely vulnerable latches
C++
AIGER circuit
[TestCase(s)]
BackEnd:
Vulnerabilities:
L1, L334, …,
L9985
011??01000110
101??01100111
…
BackEnd 1
BackEnd 2
BackEnd 3
[Error-Traces]:
Latch 1:
- flip L1 at i=5
- error at i=9
- input vectors
i0: 0101
i1: 1010
...
Options
Lingeling
miniSAT
CUDD
openSEA

---
Simulation (3/3)
Simulation-based solution: Details
// Step 2: simulation with faults:
for all latches l in L:
  for all test cases t in T:
    for all time steps i=1 to len(t):
      s := correctState[i]
      s := s with L flipped
      for all time steps j=i to len(t):
        if(s == correctState[t][j])
        continue with next step i
        s,o,c := simu1step(s,t[i])
        if(alarm)
        continue with next step i
        if(o != correctOutput[t][j])
        print “Latch L is vulnerable”
        continue with next latch l
// Step 1: fault-free simulation
for all test cases t in T:
  s := initial state
  for all time steps i=1 to len(t):
    correctState[t][i] := s
    s,o := sim1step(s,t[i])
    correctOutput[t][i] := o

---
Semi-Formal approach
- SAT-based: symbolically encode the circuit as a formula
- test case-based: Input values from test cases, can be concrete or open
- 2 variants:
  - A) point in time to flip symbolic:
  - B) point in time AND component to flip symbolic
011??01000110
101??01100111
…
for all test cases t in T:
  for all latches l in L:
    for all time steps i=1 to len(t):
      // check ...
for all test cases t in T:
  for all latches l in L:
    for all time steps i=1 to len(t):
      // check ...

---
A) point in time to flip symbolic:
for all test cases t in T:
  for all latches l in L:
    for all time steps i=1 to len(t):
      // check ...
- If SATISFIABLE:
  - Flip L in step 1 to produce corrupt outputs
timestep 0:
timestep 1:
L(0)
L(1)
0
1
0
1
0
1
replaced
Latch-output
replaced
Latch-output
f0
f1
fn
assignment: ¬f0, f1, ¬f2, .. , ¬fn

---
Environment Models
- Output values might be irrelevant
  - e.g. if data on bus is not ready
- Some input combinations might not be allowed
  - SAT-solver choices for input values can
    be restricted

---
Results – Length of Test Cases

---
Vulnerable Latches:
NO
Given: circuit
time
Input
Output
State
Next
State
clock
Alarm

---
Vulnerable Latches:
NO
- Given: circuit
- Find situation..
  - where Latch can be flipped ...
no alarm raised
time
flip
Input
Output
State
Next
State
clock
Alarm

---
Vulnerable Latches:
NO
- Given: circuit
- Find situation..
  - where Latch can be flipped ...
  - such that outputs are wrong
  - without raising an alarm before
no alarm raised
time
flip
output
different
Input
Output
State
Next
State
clock
Alarm