Soft-Error-Analysis

---
Typical Synthesis Flow
Overview
- Previously … [recap]
  - Introduction: Soft-Errors & Soft-Error Analysis
  - Detect Soft-Errors
  - Verify Protection Logic (vulnerabilities)
- Latest work:
  - Verify Protection Logic (false positives)
  - Environment Models
  - Benchmark Results
- Conclusion
Internship
Summer '15
Master-Project

---
Soft Errors
- Boolean circuits: inputs, AND gates, latches, outputs
- Components (latches, AND gates) can have soft-errors
  - flip truth value

---
How to detect Soft-Errors?
L1
L2
Outputs
...
...
Inputs
Ln
...

---
How to detect Soft-Errors:
→ add redundancy. Tool: AddParityTool
L1
⊕
Inputs
L2
Outputs
...
...
⊕
Alarm Output
Ln
⊕
Le1
⊕
⊕
...

---
Q: Is the protection-circuit correct ... ?
- Given: Circuit
- Find Vulnerabilities:
  - Latches that can be flipped (once)
  - such that output changes (at some point in the future)
  - but no alarm raised (up to that point)
?
?
?
no alarm raised
flip
output
different

---
Model Checking Approach
- Tool: AlarmToMC
Circuit
Output1
Input
Next
State
Alarm
E (“soft error
escaped”)
clock
State
Copy
Output2
Input
Alarm
Next
State
clock
clock
State

---
Model Checking Approach
- Contra:
  - Bad scalability
- Pro:
  - Exact: Valid for all possible input combinations

---
Model Checking Approach
- Contra:
  - Bad scalability
- Pro:
  - Exact: Valid for all possible input combinations
Idea: Instead of all possible Input combinations, use concrete input vectors

---
openSEA
- Input: arbitrary circuit with protection logic (alarm output)
- Output: List of definitely vulnerable latches
C++
AIGER circuit
[TestCase(s)]
BackEnd:
Vulnerabilities:
L1, L334, …,
L9985
011??01000110
101??01100111
…
BackEnd 1
BackEnd 2
BackEnd 3
[Error-Traces]:
Latch 1:
- flip L1 at i=5
- error at i=9
- input vectors
i0: 0101
i1: 1010
...
Options
Lingeling
miniSAT
PicoSAT
openSEA

---
BackEnds
- Simulation – based: (SIM)
  - Execute correct simulation with the provided TestCase
  - Compare with all possible faulty simulations
- Symbolic Time Analysis: (STA)
  - Point in time when to flip a latch is symbolic
- Symbolic Time + Symbolic Location (STLA)
  - Point in Time + Latch to flip is component

---
Latest Work
- False Positives
- Environment Models
- Benchmark Results

---
False Positives
- Vulnerabilities are false negatives: a soft error happens, but is not detected
  - Alarm should have been raised
- False Positive: Alarm is true, but the soft-error has no effect
  - Alarm raised gratuitously
no alarm raised
flip
output
different
somewhere: alarm= 1
outputs OK
flip
state normal again

---
False Positives
- Implemented similar to Algorithms for false-negatives:
  - Symbolic Time Analysis (STA)
  - Symbolic Time Symbolic Location Analysis (STLA)
somewhere: alarm= 1
outputs OK
flip
state normal again

---
Environment Models
- Output values might be irrelevant
  - e.g. if data on bus is not ready
- Some input combinations might not be allowed
  - SAT-solver choices for input values can
    be restricted

---
Benchmark Results – Setup for Experiments
- IWLS 2002 and IWL 2005 [1] circuits converted to AIGER format
- Add protection (AddParityTool)
  - only parity
  - Parameters:
    - Percentage of latches to protect
    - Number of latches to protect with 1 new latch
- Test Inputs: created randomly
                  [1] http://www.eecs.berkeley.edu/~alanmi/benchmarks/
011??01000110
101??01100111
…

---
Results – All Algorithms

---
Results – Length of Test Cases

---
Optimization: Unsatisfiable Cores

---
Number of unspecified input values

---
Model Checking Results

---
Conclusion
- Extended openSEA
  - False Positives Algorithms
    - Symbolic Time
    - Symbolic Time + symbolic Location
  - Environment Models
- Benchmarking results
  - Free inputs: sym. Algorithms (STLA) scale significantly better than simulation
  - Concrete Inputs: Simulation is fastest
  - Reducing input space: better than MC
  - UNSAT cores might speed up longer test cases
Completeness
Scalability
All Inputs Fixed	Some Inputs Open	All Inputs Open
Simulation		Model Checking
Our Approach